## Slide 1
Instructors:
Class 1: Chen Xiangqun, Sun Guangyu, Liu Xianhua
Class 2: Guan Xuetao
Class 3: Lu Junlin
Processor Architecture I: ISA & Logic Design Introduction to Computer Systems 9th Lecture, Oct 18, 2021

## Slide 2: Part A Instruction Set Architecture

## Slide 3: Instruction Set Architecture
Assembly Language View
  Processor state
    Registers, memory, …
  Instructions
    addq, pushq, ret, …
    How instructions are encoded as bytes
Layer of Abstraction
  Above: how to program machine
    Processor executes instructions in a sequence
  Below: what needs to be built
    Use variety of tricks to make it run fast
    E.g., execute multiple instructions simultaneously
ISA
Compiler
OS
CPU
Design
Circuit
Design
Chip
Layout
Application
Program

## Slide 4: Y86-64 Processor State
ZF
SF
OF
  Program Registers
    15 registers (omit %r15). Each 64 bits
  Condition Codes
    Single-bit flags set by arithmetic or logical instructions
      ZF: Zero SF:Negative OF: Overflow
  Program Counter
    Indicates address of next instruction
  Program Status
    Indicates either normal operation or some error condition
  Memory
    Byte-addressable storage array
    Words stored in little-endian byte order
RF: Program registers
CC: Condition codes
PC
DMEM: Memory
Stat: Program status
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%rax
%rcx
%rdx
%rbx
%rsp
%rbp
%rsi
%rdi

## Slide 5: Y86-64 Instruction Set #1
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9

## Slide 6: Y86-64 Instructions
Format
  1–10 bytes of information read from memory
    Can determine instruction length from first byte
    Not as many instruction types, and simpler encoding than with x86-64
  Each accesses and modifies some part(s) of the program state

## Slide 7: Y86-64 Instruction Set #2
0
1
2
3
4
5
6
7
8
9
V
D
D
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
rmmovq rA, D(rB)
4
0
rA
rB
mrmovq D(rB), rA
5
0
rA
rB
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
rrmovq
2
0
cmovle
2
1
cmovl
2
2
cmove
2
3
cmovne
2
4
cmovge
2
5
cmovg
2
6

## Slide 8: Y86-64 Instruction Set #3
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
addq
6
0
subq
6
1
andq
6
2
xorq
6
3

## Slide 9: Y86-64 Instruction Set #4
Byte
pushq rA
A
0
rA
F
jXX Dest
7
fn
Dest
popq rA
B
0
rA
F
call Dest
8
0
Dest
cmovXX rA, rB
2
fn
rA
rB
irmovq V, rB
3
0
F
rB
V
rmmovq rA, D(rB)
4
0
rA
rB
D
mrmovq D(rB), rA
5
0
rA
rB
D
OPq rA, rB
6
fn
rA
rB
ret
9
0
nop
1
0
halt
0
0
0
1
2
3
4
5
6
7
8
9
jmp
7
0
jle
7
1
jl
7
2
je
7
3
jne
7
4
jge
7
5
jg
7
6

## Slide 10: Encoding Registers
Each register has 4-bit ID
  Same encoding as in x86-64
Register ID 15 (0xF) indicates “no register”
  Will use this in our hardware design in multiple places
%rax
%rcx
%rdx
%rbx
0
1
2
3
%rsp
%rbp
%rsi
%rdi
4
5
6
7
%r8
%r9
%r10
%r11
8
9
A
B
%r12
%r13
%r14
No Register
C
D
E
F

## Slide 11: Instruction Example
Addition Instruction
  Add value in register rA to that in register rB
    Store result in register rB
    Note that Y86-64 only allows addition to be applied to register data
  Set condition codes based on result
  e.g., addq %rax,%rsi Encoding: 60 06
  Two-byte encoding
    First indicates instruction type
    Second gives source and destination registers
addq rA, rB
6
0
rA
rB
Encoded Representation
Generic Form

## Slide 12: Arithmetic and Logical Operations
  Refer to generically as “OPq”
  Encodings differ only by “function code”
    Low-order 4 bytes in first instruction word
  Set condition codes as side effect
addq rA, rB
6
0
rA
rB
subq rA, rB
6
1
rA
rB
andq rA, rB
6
2
rA
rB
xorq rA, rB
6
3
rA
rB
Add
Subtract (rA from rB)
And
Exclusive-Or
Instruction Code
Function Code

## Slide 13: Move Operations
  Like the x86-64 movq instruction
  Simpler format for memory addresses
  Give different names to keep them distinct
rrmovq rA, rB
2
0
Register  Register
Immediate  Register
irmovq V, rB
F
rB
3
0
V
Register  Memory
rmmovq rA, D(rB)
4
0
rA
rB
D
Memory  Register
mrmovq D(rB), rA
5
0
rA
rB
D
rA
rB

## Slide 14: Move Instruction Examples
irmovq $0xabcd, %rdx
movq $0xabcd, %rdx
30 f2 cd ab 00 00 00 00 00 00
X86-64
Y86-64
Encoding:
rrmovq %rsp, %rbx
movq %rsp, %rbx
20 43
mrmovq -12(%rbp),%rcx
movq -12(%rbp),%rcx
50 15 f4 ff ff ff ff ff ff ff
rmmovq %rsi,0x41c(%rsp)
movq %rsi,0x41c(%rsp)
40 64 1c 04 00 00 00 00 00 00
Encoding:
Encoding:
Encoding:

## Slide 15: Conditional Move Instructions
  Refer to generically as “cmovXX”
  Encodings differ only by “function code”
  Based on values of condition codes
  Variants of rrmovq instruction
    (Conditionally) copy value from source to destination register
rrmovq rA, rB
Move Unconditionally
cmovle rA, rB
Move When Less or Equal
cmovl rA, rB
Move When Less
cmove rA, rB
Move When Equal
cmovne rA, rB
Move When Not Equal
cmovge rA, rB
Move When Greater or Equal
cmovg rA, rB
Move When Greater
2
0
rA
rB
2
1
rA
rB
2
2
rA
rB
2
3
rA
rB
2
4
rA
rB
2
5
rA
rB
2
6
rA
rB

## Slide 16: Jump Instructions
  Refer to generically as “jXX”
  Encodings differ only by “function code” fn
  Based on values of condition codes
  Same as x86-64 counterparts
  Encode full destination address
    Unlike PC-relative addressing seen in x86-64
jXX Dest
7
fn
Jump (Conditionally)
Dest

## Slide 17: Jump Instructions
jmp Dest
7
0
Jump Unconditionally
Dest
jle Dest
7
1
Jump When Less or Equal
Dest
jl Dest
7
2
Jump When Less
Dest
je Dest
7
3
Jump When Equal
Dest
jne Dest
7
4
Jump When Not Equal
Dest
jge Dest
7
5
Jump When Greater or Equal
Dest
jg Dest
7
6
Jump When Greater
Dest

## Slide 18: Y86-64 Program Stack
  Region of memory holding program data
  Used in Y86-64 (and x86-64) for supporting procedure calls
  Stack top indicated by %rsp
    Address of top stack element
  Stack grows toward lower addresses
    Top element is at highest address in the stack
    When pushing, must first decrement stack pointer
    After popping, increment stack pointer
%rsp
•
•
•
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 19: Stack Operations
  Decrement %rsp by 8
  Store word from rA to memory at %rsp
  Like x86-64
  Read word from memory at %rsp
  Save in rA
  Increment %rsp by 8
  Like x86-64
pushq rA
A
0
rA
F
popq rA
B
0
rA
F

## Slide 20: Subroutine Call and Return
  Push address of next instruction onto stack
  Start executing instructions at Dest
  Like x86-64
  Pop value from stack
  Use as address for next instruction
  Like x86-64
call Dest
8
0
Dest
ret
9
0

## Slide 21: Miscellaneous Instructions
  Don’t do anything
  Stop executing instructions
  x86-64 has comparable instruction, but can’t execute it in user mode
  We will use it to stop the simulator
  Encoding ensures that program hitting memory initialized to zero will halt
nop
1
0
halt
0
0

## Slide 22: Status Conditions
Mnemonic | Code
ADR | 3
Mnemonic | Code
INS | 4
Mnemonic | Code
HLT | 2
Mnemonic | Code
AOK | 1
  Normal operation
  Halt instruction encountered
  Bad address (either instruction or data) encountered
  Invalid instruction encountered
Desired Behavior
  If AOK, keep going
  Otherwise, stop program execution

## Slide 23: Writing Y86-64 Code
Try to Use C Compiler as Much as Possible
  Write code in C
  Compile for x86-64 with gcc –Og –S
  Transliterate into Y86-64
  Modern compilers make this more difficult
Coding Example
  Find number of elements in null-terminated list
    int len1(int a[]);
5043
6125
7395
0
a
 3

## Slide 24: Y86-64 Code Generation Example
First Try
  Write typical array code
  Compile with gcc -Og -S
Problem
  Hard to do array indexing on Y86-64
    Since don’t have scaled addressing modes
/* Find number of elements in
null-terminated list */
long len(long a[])
{
long len;
for (len = 0; a[len]; len++)
;
return len;
}
L3:
addq $1,%rax
cmpq $0, (%rdi,%rax,8)
jne L3

## Slide 25: Y86-64 Code Generation Example #2
Second Try
  Write C code that mimics expected Y86-64 code
Result
  Compiler generates exact same code as before!
  Compiler converts both versions into same intermediate form
long len2(long *a)
{
long ip = (long) a;
long val = *(long *) ip;
long len = 0;
while (val) {
ip += sizeof(long);
len++;
val = *(long *) ip;
}
return len;
}

## Slide 26: Y86-64 Code Generation Example #3
len:
irmovq $1, %r8 # Constant 1
irmovq $8, %r9 # Constant 8
irmovq $0, %rax # len = 0
mrmovq (%rdi), %rdx # val = *a
andq %rdx, %rdx # Test val
je Done # If zero, goto Done
Loop:
addq %r8, %rax # len++
addq %r9, %rdi # a++
mrmovq (%rdi), %rdx # val = *a
andq %rdx, %rdx # Test val
jne Loop # If !0, goto Loop
Done:
ret
Register | Use
%rdi | a
%rax | len
%rdx | val
%r8 | 1
%r9 | 8

## Slide 27: Y86-64 Sample Program Structure #1
  Program starts at address 0
  Must set up stack
    Where located
    Pointer values
    Make sure don’t overwrite code!
  Must initialize data
init: # Initialization
. . .
call Main
halt
.align 8 # Program data
array:
. . .
Main: # Main function
. . .
call len . . .
len: # Length function
. . .
.pos 0x100 # Placement of stack
Stack:

## Slide 28: Y86-64 Program Structure #2
  Program starts at address 0
  Must set up stack
  Must initialize data
  Can use symbolic names
init:
# Set up stack pointer
irmovq Stack, %rsp
# Execute main program
  call Main
  # Terminate
  halt
# Array of 4 elements + terminating 0
.align 8
Array:
.quad 0x000d000d000d000d
  .quad 0x00c000c000c000c0
.quad 0x0b000b000b000b00
.quad 0xa000a000a000a000
.quad 0

## Slide 29: Y86-64 Program Structure #3
Set up call to len
  Follow x86-64 procedure conventions
  Push array address as argument
Main:
irmovq array,%rdi
# call len(array)
call len
ret

## Slide 30: Assembling Y86-64 Program
  Generates “object code” file len.yo
    Actually looks like disassembler output
  unix> yas len.ys
  0x054: | len:
  0x054: 30f80100000000000000 | irmovq $1, %r8 # Constant 1
  0x05e: 30f90800000000000000 | irmovq $8, %r9 # Constant 8
  0x068: 30f00000000000000000 | irmovq $0, %rax # len = 0
  0x072: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x07c: 6222 | andq %rdx, %rdx # Test val
  0x07e: 73a000000000000000 | je Done # If zero, goto Done
  0x087: | Loop:
  0x087: 6080 | addq %r8, %rax # len++
  0x089: 6097 | addq %r9, %rdi # a++
  0x08b: 50270000000000000000 | mrmovq (%rdi), %rdx # val = *a
  0x095: 6222 | andq %rdx, %rdx # Test val
  0x097: 748700000000000000 | jne Loop # If !0, goto Loop
  0x0a0: | Done:
  0x0a0: 90 | ret

## Slide 31: Simulating Y86-64 Program
  Instruction set simulator
    Computes effect of each instruction on processor state
    Prints changes in state from original
  unix> yis len.yo
  Stopped in 33 steps at PC = 0x13. Status 'HLT', CC Z=1 S=0 O=0
  Changes to registers:
  %rax: 0x0000000000000000 0x0000000000000004
  %rsp: 0x0000000000000000 0x0000000000000100
  %rdi: 0x0000000000000000 0x0000000000000038
  %r8: 0x0000000000000000 0x0000000000000001
  %r9: 0x0000000000000000 0x0000000000000008
  Changes to memory:
  0x00f0: 0x0000000000000000 0x0000000000000053
  0x00f8: 0x0000000000000000 0x0000000000000013

## Slide 32: CISC Instruction Sets
  Complex Instruction Set Computer
  IA32 is example
Stack-oriented instruction set
  Use stack to pass arguments, save program counter
  Explicit push and pop instructions
Arithmetic instructions can access memory
  addq %rax, 12(%rbx,%rcx,8)
    requires memory read and write
    Complex address calculation
Condition codes
  Set as side effect of arithmetic and logical instructions
Philosophy
  Add instructions to perform “typical” programming tasks

## Slide 33: RISC Instruction Sets
  Reduced Instruction Set Computer
  Internal project at IBM, later popularized by Hennessy (Stanford) and Patterson (Berkeley)
Fewer, simpler instructions
  Might take more to get given task done
  Can execute them with small and fast hardware
Register-oriented instruction set
  Many more (typically 32) registers
  Use for arguments, return pointer, temporaries
Only load and store instructions can access memory
  Similar to Y86-64 mrmovq and rmmovq
No Condition codes
  Test instructions return 0/1 in register

## Slide 34: MIPS Registers

## Slide 35: MIPS Instruction Examples
Op
Ra
Rb
Offset
Op
Ra
Rb
Rd
Fn
00000
R-R
Op
Ra
Rb
Immediate
R-I
Load/Store
addu $3,$2,$1 # Register add: $3 = $2+$1
addu $3,$2, 3145 # Immediate add: $3 = $2+3145
sll $3,$2,2 # Shift left: $3 = $2 << 2
lw $3,16($2) # Load Word: $3 = M[$2+16]
sw $3,16($2) # Store Word: M[$2+16] = $3
Op
Ra
Rb
Offset
Branch
beq $3,$2,dest # Branch when $3 = $2

## Slide 36: CISC vs. RISC
Original Debate
  Strong opinions!
  CISC proponents---easy for compiler, fewer code bytes
  RISC proponents---better for optimizing compilers, can make run fast with simple chip design
Current Status
  For desktop processors, choice of ISA not a technical issue
    With enough hardware, can make anything run fast
    Code compatibility more important
  x86-64 adopted many RISC features
    More registers; use them for argument passing
  For embedded processors, RISC makes sense
    Smaller, cheaper, less power
    Most cell phones use ARM processor

## Slide 37: Summary
Y86-64 Instruction Set Architecture
  Similar state and instructions as x86-64
  Simpler encodings
  Somewhere between CISC and RISC
How Important is ISA Design?
  Less now than before
    With enough hardware, can make almost anything go fast

## Slide 38: Part B Logic Design

## Slide 39: Overview of Logic Design
Fundamental Hardware Requirements
  Communication
    How to get values from one place to another
  Computation
  Storage
Bits are Our Friends
  Everything expressed in terms of values 0 and 1
  Communication
    Low or high voltage on wire
  Computation
    Compute Boolean functions
  Storage
    Store bits of information

## Slide 40: Digital Signals
  Use voltage thresholds to extract discrete values from continuous signal
  Simplest version: 1-bit signal
    Either high range (1) or low range (0)
    With guard range between them
  Not strongly affected by noise or low quality circuit elements
    Can make circuits simple, small, and fast
Voltage
Time
0
1
0

## Slide 41: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a && b
Rising Delay
Falling Delay

## Slide 42: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 43: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language
    Boolean operations have syntax similar to C logical operations
  We’ll use it to describe control logic for processors
Bit equal
a
b
eq
bool eq = (a&&b)||(!a&&!b)
HCL Expression

## Slide 44: Word Equality
  64-bit word size
  HCL representation
    Equality operation
    Generates Boolean value
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 45: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 46: Word Multiplexor
  Select input word A or B depending on control signal s
  HCL representation
    Case expression
    Series of test : value pairs
    Output value for first successful test
Word-Level Representation
HCL Representation
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
int Out = [
s : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 47: HCL Word-Level Examples
  Find minimum of three input words
  HCL case expression
  Final case guarantees match
A
Min3
MIN3
B
C
int Min3 = [
A < B && A < C : A;
B < A && B < C : B;
1 : C;
];
D0
D3
Out4
s0
s1
MUX4
D2
D1
  Select one of 4 inputs based on two control bits
  HCL case expression
  Simplify tests by assuming sequential matching
int Out4 = [
!s1&&!s0: D0;
!s1 : D1;
!s0 : D2;
1 : D3;
];
Minimum of 3 Words
4-Way Multiplexor

## Slide 48: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86-64
  Also computes values for condition codes
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 49: Registers
  Stores word of data
    Different from program registers seen in assembly code
  Collection of edge-triggered latches
  Loads input on rising edge of clock
I
O
Clock
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 50: Register Operation
  Stores data bits
  For most of time acts as barrier between input and output
  As clock rises, loads input
State = x
Rising
clock

Output = x
Input = y
x

State = y
Output = y
y

## Slide 51: State Machine Example
  Accumulator circuit
  Load or accumulate on each cycle
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
x0
x1
x2
x3
x4
x5
x0
x0+x1
x0+x1+x2
x3
x3+x4
x3+x4+x5
Clock
Load
In
Out

## Slide 52: Random-Access Memory
  Stores multiple words of memory
    Address input specifies which word to read or write
  Register file
    Holds values of program registers
    %rax, %rsp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple words in one cycle
      Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 53: Register File Timing
Reading
  Like combinational logic
  Output data generated based on input address
    After some delay
Writing
  Like register
  Update only as clock rises
Register
file
A
B
srcA
valA
srcB
valB
y
2
Register
file
W
dstW
valW
Clock
x
2
Rising
clock


Register
file
W
dstW
valW
Clock
y
2
x
2
x
2

## Slide 54: Hardware Control Language
  Very simple hardware description language
  Can only express limited aspects of hardware operation
    Parts we want to explore and modify
Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    Does not specify word size---bytes, 64-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 55: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 56: Summary
Computation
  Performed by combinational logic
  Computes Boolean functions
  Continuously reacts to input changes
Storage
  Registers
    Hold single words
    Loaded as clock rises
  Random-access memories
    Hold multiple words
    Possible multiple read or write ports
    Read word when address input changes
    Write word as clock rises

## Slide 57: Additional Slides

## Slide 58: Storing 1 Bit
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2

## Slide 59: Storing 1 Bit (cont.)
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2
Vin
V1
V2
Vin = V2
Stable 0
Stable 1
Metastable

## Slide 60: Physical Analogy
Stable 0
Stable 1
Metastable
.
Stable left
.
Stable right
.
Metastable

## Slide 61: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 62: 1-Bit Latch
D Latch
Q+
Q–
R
S
D
C
Data
Clock
Latching
1
d
!d
!d
!d
d
d
d
!d
0
Storing
d
!d
q
!q
!q
q
0
0

## Slide 63: Transparent 1-Bit Latch
  When in latching mode, combinational propogation from D to Q+ and Q–
  Value latched depends on value of D as C falls
C
D
Q+
Time
Changing D
Latching
1
d
!d
!d
!d
d
d
d
!d

## Slide 64: Edge-Triggered Latch
  Only in latching mode for brief period
    Rising clock edge
  Value latched depends on data as clock rises
  Output remains stable at all other times
Q+
Q–
R
S
D
C
Data
Clock
T
Trigger
C
D
Q+
Time
T